3. Methodology

The methodology of this project describes the systematic approach used to design and implement a smart fish detection and water monitoring system by integrating embedded hardware, IoT communication, and artificial intelligence techniques. The system is developed using an ESP32-S3 CAM module for data acquisition and a Python-based server using the Flask framework for processing and visualization.
The ESP32-S3 collects real-time environmental data from multiple sensors, including water temperature, surface temperature, water level, pressure, and turbidity. It also captures live video streams of the aquatic environment using an onboard camera. This data is transmitted over a Wi-Fi network to a local server for further processing.
On the server side, a Flask-based web application is used to handle data communication and visualization. The live video stream received from the ESP32 is processed using OpenCV, and object detection is performed using a pre-trained YOLO (You Only Look Once) deep learning model. This enables real-time identification and tracking of fish in the captured frames.
Sensor data is periodically fetched from the ESP32 and integrated with the detection results to provide a unified monitoring system. The processed information is displayed on a dynamic web dashboard, allowing users to observe both environmental parameters and fish activity in real time.
This methodology ensures efficient data acquisition, intelligent processing, and user-friendly visualization, resulting in a robust and automated system for aquaculture monitoring. By combining IoT and AI technologies, the system enhances accuracy, reduces manual effort, and enables better decision-making in aquatic environments.
## Block Diagram Description
The block diagram represents the overall architecture of the smart fish detection and water monitoring system. At the core of the system is the ESP32-S3 microcontroller, which acts as the main processing and control unit. It interfaces with multiple sensors and modules to collect environmental data and manage system operations.
The JNS-SR04T ultrasonic sensor is used to measure the water level or distance by calculating the time taken for ultrasonic waves to reflect from the surface. The DS18B20 temperature sensor is used to measure water temperature accurately, while the DHT11 sensor measures ambient temperature and humidity. The BMP180 sensor is used to measure atmospheric pressure and altitude, which helps in environmental analysis.
A turbidity sensor (water quality sensor) is used to determine the clarity of water, which is an important parameter for fish health. All these sensors continuously send data to the ESP32-S3 for processing.
The ESP32-S3 CAM module also includes a camera that captures real-time images or video of the aquatic environment. A power module is used to supply stable voltage to all components, ensuring reliable operation.
The processed data is then transmitted via Wi-Fi to external devices such as a laptop or mobile device, where it can be visualized through a web interface. This architecture enables real-time monitoring and intelligent decision-making.
Fig-3.1: Block Diagram
## Workflow Description
The workflow of the system illustrates the step-by-step operation from data collection to user visualization. Initially, the sensors connected to the ESP32-S3 collect environmental parameters such as water temperature, surface temperature, water level, turbidity, and pressure. At the same time, the onboard camera captures live video of the aquatic environment.
Once the data is collected, the ESP32-S3 processes the sensor readings and streams the video through a Wi-Fi network. The data is transmitted using HTTP protocols to a local server system.
On the receiving side, a Python-based Flask server processes the incoming data. The video stream is decoded using OpenCV, and a YOLO deep learning model is applied to detect and identify fish in real time. The detection results, along with sensor data, are combined and updated continuously.
The processed data is then displayed on a web-based dashboard, which includes live video feed with detection overlays, sensor readings, and system status indicators. Users can access this dashboard through a laptop or mobile device.
The entire workflow operates continuously in a loop, enabling real-time monitoring, early detection of issues, and improved management of aquaculture environments.

Fig-3.2: Workflow Diagram
Software Description
The software component of the proposed smart fish detection and water monitoring system plays a crucial role in data processing, communication, visualization, and intelligent analysis. The system integrates multiple software tools and frameworks, including embedded programming, web development, and artificial intelligence libraries, to achieve real-time monitoring and automation.
### Embedded Programming (Arduino IDE)
The ESP32-S3 microcontroller is programmed using the Arduino IDE, which provides a simple and efficient environment for developing embedded applications. The firmware is responsible for interfacing with various sensors such as DS18B20, DHT11, ultrasonic sensor, BMP180, and turbidity sensor. It collects real-time environmental data, processes basic calculations, and manages communication over Wi-Fi. The ESP32 also handles camera initialization and streams image data through HTTP protocols.
### Python and Flask Framework
A Python-based server is implemented using the Flask framework to handle backend processing and communication. Flask acts as a lightweight web server that receives data from the ESP32-S3 and provides API endpoints for accessing sensor data and video streams. It manages routing, data handling, and integration between different components of the system. The server continuously fetches sensor data and processes incoming video frames for further analysis.
### OpenCV (Computer Vision Library)
OpenCV is used for real-time image processing and video stream handling. It decodes the incoming MJPEG stream from the ESP32 camera and converts it into frames suitable for analysis. OpenCV is also used to draw bounding boxes, labels, and overlays on detected objects, enhancing visualization and interpretation of results.
### YOLO (Deep Learning Model)
The system uses a YOLO (You Only Look Once) model for object detection, specifically trained to detect fish or marine objects. YOLO is a real-time object detection algorithm known for its speed and accuracy. It processes each video frame and identifies objects by generating bounding boxes and class labels. The detection results are used to monitor fish presence and activity in the aquatic environment.
### Frontend Web Technologies
The user interface is developed using HTML, CSS, and JavaScript. The web dashboard provides a real-time visualization of sensor data and live video feed. Chart.js is used for plotting graphs such as water level trends, while JavaScript handles dynamic updates and asynchronous data fetching from the Flask server. The interface is designed to be responsive and accessible from both desktop and mobile devices.
### Communication Protocols
The system uses HTTP-based communication for data exchange between the ESP32-S3 and the Flask server. Sensor data is transmitted in JSON format through API endpoints, while the video stream is delivered using MJPEG streaming. This approach ensures efficient and real-time data transfer over a Wi-Fi network.
## ESP32-S3 CAM Module
The ESP32-S3 CAM module is the core hardware component of the proposed smart fish detection and water monitoring system. It is a powerful microcontroller unit developed by Espressif Systems, featuring integrated Wi-Fi and enhanced processing capabilities suitable for embedded vision and IoT applications. The module is specifically designed to support camera-based applications while maintaining low power consumption and compact size.
The ESP32-S3 is built on a dual-core processor architecture, which enables efficient multitasking and real-time data processing. It includes sufficient GPIO pins to interface with various sensors such as temperature sensors, ultrasonic sensors, turbidity sensors, and pressure sensors. In addition, it supports communication protocols such as I2C, SPI, and UART, allowing seamless integration with multiple hardware components.
One of the key features of the ESP32-S3 CAM module is its compatibility with camera sensors such as the OV3660. This allows the system to capture images and stream video in real time. The module supports JPEG image compression, which reduces data size and enables efficient transmission over Wi-Fi networks. This feature is particularly important for real-time monitoring applications where bandwidth optimization is required.
The built-in Wi-Fi capability of the ESP32-S3 enables wireless communication with external devices such as laptops, mobile phones, or cloud servers. In this project, the ESP32-S3 acts as a web server that transmits sensor data and live video streams to a Flask-based application for further processing and visualization.
The module also supports external PSRAM, which enhances its ability to handle large image buffers and improves overall performance during video streaming and image processing tasks. This makes it suitable for applications involving computer vision and real-time monitoring.
Furthermore, the ESP32-S3 CAM module operates at low power and can be powered using a regulated power supply, making it suitable for continuous operation in aquaculture environments. Its compact design, processing capability, and wireless connectivity make it an ideal choice for integrating sensing, processing, and communication in a single platform.

## Ultrasonic Sensor (JNS-SR04T)
The JNS-SR04T ultrasonic sensor is used in this project to measure the distance between the sensor and the water surface, which helps in determining the water level in the pond or tank. It is a waterproof ultrasonic distance sensor, making it highly suitable for outdoor and aquatic environments where exposure to moisture is common.
The sensor operates on the principle of ultrasonic wave propagation. It consists of a transmitter and a receiver. The transmitter emits high-frequency ultrasonic sound waves (typically around 40 kHz), which travel through the air and reflect back when they encounter an object, such as the water surface. The receiver detects the reflected signal, and the time taken for the wave to return is used to calculate the distance.
The distance is calculated using the time-of-flight principle, based on the speed of sound in air. The ESP32-S3 microcontroller sends a trigger pulse to the sensor, which initiates the transmission of ultrasonic waves. When the echo signal is received, the duration of the pulse is measured, and the distance is computed using a mathematical formula.
The JNS-SR04T sensor is capable of measuring distances typically ranging from 20 cm to 600 cm with reasonable accuracy. Its waterproof probe design ensures reliable performance in humid or wet conditions, unlike standard ultrasonic sensors that are sensitive to moisture.
In this system, the sensor is mounted above the water surface, and the measured distance is used to estimate the water level. By comparing the measured distance with the known height of the tank or pond, the system can determine whether the water level is within the desired range.
The sensor provides a digital output in the form of a pulse signal, which is easily interfaced with the ESP32-S3 through GPIO pins. Its low cost, ease of use, and robustness make it an ideal choice for real-time water level monitoring in aquaculture applications.
## DS18B20 Temperature Sensor
The DS18B20 is a digital temperature sensor used in this project to measure the water temperature accurately. It is widely used in embedded and IoT applications due to its high precision, reliability, and ease of interfacing. The sensor is particularly suitable for aquatic environments because it is available in a waterproof probe form, making it ideal for direct immersion in water.
The DS18B20 operates using the One-Wire communication protocol, which allows data transmission through a single data line along with ground. This reduces wiring complexity and enables multiple sensors to be connected to the same microcontroller pin if required. Each DS18B20 sensor has a unique 64-bit serial code, allowing multiple devices to operate on the same bus without conflict.
The sensor provides digital temperature readings with a high degree of accuracy, typically ±0.5°C over a wide temperature range of -55°C to +125°C. In this project, it is primarily used within the range suitable for aquaculture, where maintaining optimal water temperature is essential for fish health and growth.
The DS18B20 measures temperature internally and converts the reading into a digital signal, eliminating the need for external analog-to-digital conversion. The measured data is then transmitted to the ESP32-S3 microcontroller, where it is processed and displayed on the monitoring system.
In the proposed system, the DS18B20 sensor is used to continuously monitor the water temperature, which is a critical parameter in aquaculture. Sudden changes in water temperature can stress fish and affect their metabolism, feeding behavior, and overall health. By providing real-time temperature data, the system enables timely intervention and better environmental control.
The sensor is easy to interface with the ESP32-S3 using a pull-up resistor and compatible libraries, making it a cost-effective and efficient solution for temperature monitoring. Its durability, accuracy, and waterproof design make it highly suitable for long-term deployment in water monitoring applications.

## DHT11 Temperature and Humidity Sensor
The DHT11 is a low-cost digital sensor used to measure ambient temperature and humidity. In this project, it is utilized to monitor the surface environmental conditions around the aquaculture system. Understanding atmospheric temperature and humidity is important, as these factors can influence water temperature, evaporation rates, and overall environmental stability.
The DHT11 sensor consists of a thermistor for measuring temperature and a capacitive humidity sensor for detecting moisture levels in the air. It also includes an internal microcontroller that processes the measured data and outputs it as a digital signal. This eliminates the need for external signal conditioning or analog-to-digital conversion.
The sensor communicates with the ESP32-S3 microcontroller using a single-wire digital communication protocol. It sends data in the form of a timed pulse sequence, which is decoded by the microcontroller to obtain temperature and humidity values. The DHT11 is easy to interface and requires only one data pin along with power and ground connections.
The DHT11 provides temperature measurements in the range of 0°C to 50°C with an accuracy of approximately ±2°C, and humidity measurements from 20% to 90% with an accuracy of ±5%. Although it is not as precise as advanced sensors, it is sufficient for general environmental monitoring in aquaculture systems.
In this system, the DHT11 sensor is used to monitor surface temperature conditions, which can indirectly affect the water environment. Changes in atmospheric temperature can influence water temperature and oxygen levels, thereby impacting fish health. By monitoring these conditions, the system can provide a more comprehensive understanding of the surrounding environment.
The sensor is compact, energy-efficient, and cost-effective, making it suitable for continuous monitoring applications. Its simplicity and ease of integration with the ESP32-S3 make it an ideal choice for basic environmental sensing in this project.
## Turbidity Sensor (Water Quality Sensor)
The turbidity sensor is used in this project to measure the clarity of water, which is an important indicator of water quality in aquaculture systems. Turbidity refers to the presence of suspended particles such as dirt, algae, and organic matter in water. High turbidity levels can reduce light penetration, affect photosynthesis, and negatively impact fish health.
The sensor operates based on the principle of light scattering. It consists of a light source, typically an infrared (IR) LED, and a photodetector. When light passes through water, suspended particles scatter the light. The amount of scattered light detected by the sensor is proportional to the turbidity level of the water. Clear water allows more light to pass through, while turbid water causes more scattering and reduces transmitted light intensity.
In this project, the turbidity sensor provides a digital output indicating the quality of water. The ESP32-S3 reads this signal through a GPIO pin and classifies the water condition as either “Good” or “Bad” based on predefined thresholds. This simplifies real-time monitoring and enables quick decision-making.
Turbidity is a critical parameter in aquaculture, as poor water quality can lead to reduced oxygen levels, increased stress in fish, and higher susceptibility to diseases. Continuous monitoring of turbidity helps in maintaining optimal conditions for fish growth and survival.
The sensor is easy to interface with the ESP32-S3 and requires minimal calibration for basic applications. It is cost-effective and suitable for real-time monitoring systems. By integrating turbidity measurement into the system, the project enhances its capability to assess overall water quality and ensures a healthier aquatic environment.
## BMP180 Pressure Sensor
The BMP180 is a digital barometric pressure sensor used in this project to measure atmospheric pressure and estimate altitude. It is a high-precision, low-power sensor widely used in embedded systems and environmental monitoring applications. In aquaculture systems, pressure and altitude measurements can provide useful insights into environmental conditions and weather changes.
The BMP180 sensor operates based on the piezoresistive principle, where changes in atmospheric pressure cause deformation in an internal sensing element. This deformation results in a change in electrical resistance, which is measured and converted into a digital signal. The sensor includes an internal analog-to-digital converter (ADC) and calibration data, ensuring accurate and stable readings.
The sensor communicates with the ESP32-S3 microcontroller using the I2C communication protocol, which allows efficient data transfer using only two wires: Serial Data (SDA) and Serial Clock (SCL). This makes it easy to integrate with other I2C-based devices in the system.
The BMP180 is capable of measuring pressure in the range of approximately 300 hPa to 1100 hPa, with high accuracy. Using pressure data, the sensor can also estimate altitude based on standard atmospheric models. In this project, altitude calculation helps in understanding environmental conditions and can be useful for calibration and reference purposes.
Although the BMP180 is not directly related to water quality, it contributes to the overall environmental monitoring system by providing additional atmospheric data. Changes in atmospheric pressure can indicate weather variations, which may indirectly affect aquaculture conditions such as temperature and oxygen levels.
The sensor is compact, energy-efficient, and reliable, making it suitable for continuous monitoring applications. Its compatibility with the ESP32-S3 and ease of integration through I2C communication make it an ideal choice for this project.

## YOLO (You Only Look Once) Object Detection Model
YOLO (You Only Look Once) is a state-of-the-art deep learning algorithm used for real-time object detection. In this project, YOLO is utilized to detect and identify fish in the video stream captured by the ESP32-S3 CAM module. Its high speed and accuracy make it suitable for real-time monitoring applications in aquaculture systems.
Unlike traditional object detection methods that perform multiple stages such as region proposal and classification separately, YOLO processes the entire image in a single pass through a convolutional neural network (CNN). This unified approach significantly reduces computation time and enables real-time performance.
The YOLO model divides an input image into a grid and predicts bounding boxes along with class probabilities for each grid cell. Each bounding box contains information about the position and size of the detected object, as well as a confidence score indicating the likelihood of detection. The model then applies non-maximum suppression to eliminate duplicate detections and retain the most accurate results.
In this project, a custom-trained YOLO model (e.g., seafish.pt) is used to specifically detect fish and marine objects. The model is loaded in the Python environment using the Ultralytics YOLO framework. Each frame from the video stream is processed, and detected objects are labeled with bounding boxes and class names using OpenCV.
The detection results are continuously updated and displayed on the web dashboard, allowing users to monitor fish presence and movement in real time. This helps in understanding fish behavior, detecting anomalies, and improving aquaculture management practices.
YOLO is highly efficient compared to other deep learning models, making it suitable for applications requiring low latency and real-time processing. Its integration into this system enhances the intelligence and automation of the monitoring process.

## Code Description
The software implementation of the proposed system consists of two main parts: the embedded code running on the ESP32-S3 CAM module and the Python-based server code using Flask. These components work together to acquire data, process it, and display it through a web interface.

### 1. ESP32-S3 Embedded Code
The embedded code is written using the Arduino framework and is responsible for sensor interfacing, data acquisition, camera handling, and wireless communication.
#### Sensor Data Acquisition
The ESP32 reads data from multiple sensors:
- DS18B20 for water temperature
- DHT11 for surface temperature
- Ultrasonic sensor for water level
- BMP180 for pressure and altitude
- Turbidity sensor for water quality
Each sensor is initialized in the setup function, and readings are continuously updated in the loop function. The ultrasonic sensor calculates distance using the time-of-flight principle, while the DS18B20 and DHT11 provide digital temperature readings.
#### Camera Initialization and Capture
The ESP32-S3 CAM initializes the OV3660 camera using predefined GPIO configurations. The camera captures image frames and encodes them in JPEG format for efficient transmission. The capture handler is responsible for sending image frames when requested by the client.
#### Web Server Implementation
An HTTP server is created on the ESP32 using the ESP-IDF HTTP server library. It defines multiple endpoints:
- / → serves the web interface
- /capture → sends camera images
- /sensors → returns sensor data in JSON format
This allows external systems to access real-time data easily.
#### Wi-Fi Communication
The ESP32 connects to a Wi-Fi network using predefined SSID and password. Once connected, it acts as a server and shares its IP address for communication with the Flask application.
### 2. Python Flask Server Code
The Python backend is implemented using the Flask framework and is responsible for processing video streams, performing object detection, and serving the dashboard.
#### Video Stream Handling
The Flask server connects to the ESP32 video stream using HTTP requests. The MJPEG stream is decoded into individual frames using OpenCV. These frames are then processed in real time.
#### Object Detection using YOLO
A pre-trained YOLO model (seafish.pt) is loaded using the Ultralytics library. Each video frame is passed through the model to detect fish and other objects. Bounding boxes and labels are drawn on the frames using OpenCV functions.
Detected object labels are stored and updated continuously to provide real-time detection results.
#### Sensor Data Fetching
The Flask server periodically fetches sensor data from the ESP32 using HTTP requests. The data is received in JSON format and stored in a global dictionary for easy access and synchronization with detection results.
#### Multithreading
A separate thread is used to continuously fetch sensor data without interrupting the video processing stream. This ensures smooth and efficient operation of the system.
#### API Endpoints
The Flask application defines several routes:
- /video → streams processed video with detection overlays
- /api/data → returns combined sensor and detection data
- / → serves the web dashboard
### 3. Frontend Code (Web Dashboard)
The frontend is developed using HTML, CSS, and JavaScript, and is rendered using Flask.
- Displays live video stream with detection overlays
- Shows real-time sensor data
- Uses JavaScript to fetch updates asynchronously
- Provides system status indicators and visualization
The dashboard updates dynamically without reloading, ensuring a smooth user experience.

## 1. Wi-Fi Connection Setup (ESP32)
const char* ssid = "bps_wifi";
const char* password = "sagabps@235";

WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
    delay(400);
    Serial.print(".");
}
Serial.println("Connected → " + WiFi.localIP().toString());
### Explanation
This code is used to connect the ESP32-S3 module to a Wi-Fi network. The SSID and password are provided, and the system continuously checks the connection status until it is successfully connected. Once connected, the ESP32 prints its IP address, which is used to access the web server and sensor data remotely.

## 2. Ultrasonic Sensor Distance Calculation
float getDistanceCM(){
  digitalWrite(TRIG_PIN, LOW);
  delayMicroseconds(2);
  digitalWrite(TRIG_PIN, HIGH);
  delayMicroseconds(10);
  digitalWrite(TRIG_PIN, LOW);

  duration = pulseIn(ECHO_PIN, HIGH);
  distance = (duration * 0.0343) / 2;
  return distance;
}
### Explanation
This function measures the distance using the ultrasonic sensor. A trigger pulse is sent, and the time taken for the echo signal to return is measured. Using the speed of sound, the distance is calculated. This value represents the water level in the tank or pond.

## 3. Sensor Data JSON Response
snprintf(json, sizeof(json),
 "{\"distance\":%.1f,\"waterTemp\":%.1f,\"surfaceTemp\":%.1f,\"pressure\":%.1f,\"altitude\":%.1f,\"turbidity\":%d,\"quality\":\"%s\"}",
 currentDistance, waterTemp, surfaceTemp, pressure_hPa, altitude_m, turbidityValue, waterQuality.c_str());
### Explanation
This code formats all sensor readings into a JSON string. JSON is used because it is lightweight and easy to transmit over HTTP. This data is later fetched by the Flask server and displayed on the dashboard.

## 4. Camera Frame Capture (ESP32)
camera_fb_t *fb = esp_camera_fb_get();
httpd_resp_send(req, (const char*)fb->buf, fb->len);
esp_camera_fb_return(fb);
### Explanation
This snippet captures an image frame from the ESP32 camera and sends it as a JPEG response to the client. After sending the frame, memory is released. This enables real-time image streaming.

## 5. Flask Video Stream Handling
stream = requests.get(STREAM_URL, stream=True, timeout=10)
bytes_data = b''
### Explanation
This code connects to the ESP32 video stream using HTTP. The stream is received as raw byte data, which is later decoded into image frames.

## 6. Frame Decoding using OpenCV
frame = cv2.imdecode(np.frombuffer(jpg, dtype=np.uint8), cv2.IMREAD_COLOR)
### Explanation
This line converts raw JPEG byte data into an image frame that can be processed using OpenCV. It is a crucial step before applying object detection.

## 7. YOLO Object Detection
results = model(frame, verbose=False)
### Explanation
This line passes the image frame into the YOLO model. The model processes the image and returns detected objects such as fish along with their bounding boxes and confidence scores.

## 8. Drawing Detection Boxes
cv2.rectangle(frame, (x1,y1), (x2,y2), (0,255,0), 2)
cv2.putText(frame, label, (x1, y1-10),
        cv2.FONT_HERSHEY_SIMPLEX, 0.6, (0,255,0), 2)
### Explanation
This code draws a rectangle around detected objects and displays their labels on the frame. This helps users visually identify fish in the video stream.

## 9. Sensor Data Fetching Thread
threading.Thread(target=sensor_poller, daemon=True).start()
### Explanation
This creates a separate thread to continuously fetch sensor data from the ESP32. Using multithreading ensures that sensor updates do not interrupt video processing.

## 10. API Data Endpoint (Flask)
@app.route('/api/data')
def data():
    return jsonify({
        **sensor_data,
        "detections": latest_detections
    })
### Explanation
This API endpoint sends combined sensor data and detection results in JSON format to the frontend. It allows real-time updates on the dashboard.

## 11. Live Dashboard Update (JavaScript)
let r = await fetch('/api/data');
let d = await r.json();
### Explanation
This JavaScript code fetches real-time data from the Flask server and updates the dashboard dynamically without reloading the page.

Circuit Diagram
The circuit diagram represents the hardware connections of the smart aquaculture monitoring system centered around the ESP32-S3 CAM module. The ESP32-S3 acts as the main controller, interfacing with multiple sensors to collect environmental data and transmit it for processing.
The DS18B20 temperature sensor is connected using the One-Wire protocol. It is interfaced with a GPIO pin of the ESP32, along with a 4.7 kΩ pull-up resistor connected between the data line and VCC to ensure proper communication. This sensor is used to measure the water temperature.
The DHT11 sensor is connected to another GPIO pin of the ESP32 for measuring ambient temperature and humidity. It operates using a single digital data line along with power and ground connections.
The ultrasonic sensor (JNS-SR04T) is connected using two GPIO pins: one for the trigger signal and one for the echo signal. The ESP32 sends a trigger pulse and receives the echo signal to calculate the distance, which is used to determine the water level.
The turbidity sensor module is connected to the ESP32 through a digital input pin. It is powered using VCC and GND, and its output pin provides a signal indicating the water quality based on turbidity levels.
The BMP180 pressure sensor is interfaced using the I2C communication protocol. The SDA (data) and SCL (clock) lines are connected to the respective I2C pins of the ESP32-S3, enabling communication for pressure and altitude measurements.
All components are powered through a regulated 3.3V supply provided by the ESP32 or an external power module. Proper grounding is maintained across all components to ensure stable operation.

Fig-3.3: Circuit Diagram
The ESP32-S3 CAM module also includes a camera interface, which captures live video of the aquatic environment. The collected sensor data and video stream are transmitted via Wi-Fi to a local server for processing and visualization.